## Slide 1
Kirk S. Kalvar
Senior Software Engineer
KAL Technology
kirk.kalvar@kal.technology
IoT QuickStart with AWS

## Slide 2: IoT Growth

## Slide 3: Problem
Highly Fragmented Industry
Lack of Open Source Solutions with Significant Adoption
Resource Constraints

## Slide 4: Why Use AWS IoT?
Experience with AWS
Configurable via Web Console, CLI, or CloudFormation
Quick Prototyping
Extensive SDK Support
Scalable
Secure
Reliable

## Slide 5: Design Goals
Keep It Simple Stupid (KISS)
Minimal Viable Product (MVP) Approach
Leverage current skill set (Java/Android/AWS)
Code Reuse

## Slide 6: AWS IoT Architecture

## Slide 7: Device Shadows Documents
Devices report their state by publishing messages in JSON format on MQTT topics. A shadow document has the following properties:
  State:
    Desired: applications write to this portion of the document to update the state
    Reported: applications read this portion of the document to determine the state
    Delta: contains the difference between the desired and reported states.
  Metadata: Information about the data stored in the state section of the document
  Timestamp: when the message was transmitted by AWS IoT
  Version: Every time the document is updated, this version number is incremented

## Slide 8: Device Shadow Document
{ "state": { "desired": { "roomTemperature": 60, "windowOpen": true }, "reported": { "roomTemperature": 60, "windowOpen": true } }, "metadata": { "desired": { "roomTemperature": { "timestamp": 1493129996 }, "windowOpen": { "timestamp": 1493129553 } } }, "version": 15, "timestamp": 1493130057 }

## Slide 9: Device Shadows Data Flow
The Thing Shadows services acts as an intermediary, allowing devices and applications to retrieve and update thing shadows.
The Thing Shadows service uses MQTT topics to facilitate communication between applications and devices.
Example MQTT topics:
$aws/things/<myiotdevice>/shadow/update
  You can update a thing shadow by publishing to the /update topic.
$aws/things/<myiotdevice>/ shadow/update/get
  You can retrieve a thing shadow by subscribing to the /get topic. This retrieves the entire document plus the delta between the desired or reported states.

## Slide 10: AWS IoT Web Console

## Slide 11: AWS IoT Rule

## Slide 12: AWS IoT Rule Actions

## Slide 13: Quick Demo
Android Mobile Temperature Application with an Open/Close Toggle and Temperature Scale
Temperature Application is configured to communicate with AWS IoT and is authenticated via AWS Cognito
We’ll show how to test basic connectivity with AWS IoT
We’ll fire the following AWS IoT Rules:
  S3 to store shadow updates
  Lambda to close the window if the window is open and temperature > 72 degrees
  Elasticsearch as a near real-time “Dashboard”
Notes: Send a simple text message
Use representative website
Use phone dialer
Use web browser

## Slide 14: Quick Demo
Android Mobile Device
AWS IoT
AWS S3
AWS Lambda
AWS Elasticsearch
MQTT
Notes: Send a simple text message
Use representative website
Use phone dialer
Use web browser

## Slide 15: Conclusion
Pro
  Minimal Investment
  Fairly Quick Prototyping
  Scalable
  Secure
  Reliable
  SDK Support
Con
  Not An Open Source Solution (Proprietary)
  Must be Familiar with AWS
  Requires Jumping Through Hoops Configuring Multiple Services

## Slide 16: Questions?

## Slide 17: References
https://github.com/kskalvar/AWS-IoT-AndroidStudio.git
http://docs.aws.amazon.com/iot/latest/developerguide/aws-iot-how-it-works.html
https://aws.amazon.com/mobile/sdk